## Slide 1
The Soil Moisture Active/Passive (SMAP) Level 4 Surface and Root-zone Soil Moisture Product
Rolf Reichle1, Gabrielle DeLannoy1,2, and Wade Crow3
1 NASA Goddard Space Flight Center Global Model and Assimilation Office
2 University of Louvain, Louvain, Belgium
3 USDA ARS Hydrology and Remote Sensing Lab
Supported by the NASA SMAP mission and the NASA Applied Sciences Program (Water Resources)

## Slide 2
Soil Moisture Active/Passive (SMAP) Mission Concept
L-band unfocused SAR and radiometer system, offset-fed 6 m light-weight deployable mesh reflector. Shared feed for:
1.2 GHz Radar 1-3 km (30% nadir gap)
HH, VV and HV
1.4 GHz Radiometer at 40 km (-3 dB)
H, V, 3rd and 4th Stokes
Conical scan, fixed incidence angle at 40°
Contiguous 1000 km swath, 2-3 days revisit
Sun-synchronous 6am/6pm orbit (680 km)
Electronic Version at http://smap.jpl.nasa.gov/Imperative/
Print Version Available (182 Pages): smap_science@jpl.nasa.gov

## Slide 3
Soil Moisture Active/Passive (SMAP) Mission Concept
L-band unfocused SAR and radiometer system, offset-fed 6 m light-weight deployable mesh reflector. Shared feed for:
1.2 GHz Radar 1-3 km (30% nadir gap)
HH, VV and HV
1.4 GHz Radiometer at 40 km (-3 dB)
H, V, 3rd and 4th Stokes
Conical scan, fixed incidence angle at 40°
Contiguous 1000 km swath, 2-3 days revisit
Sun-synchronous 6am/6pm orbit (680 km)
Electronic Version at http://smap.jpl.nasa.gov/Imperative/
Print Version Available (182 Pages): smap_science@jpl.nasa.gov

## Slide 4
Soil Moisture Active/Passive (SMAP) Mission Concept
L-band unfocused SAR and radiometer system, offset-fed 6 m light-weight deployable mesh reflector. Shared feed for:
1.2 GHz Radar 1-3 km (30% nadir gap)
HH, VV and HV
1.4 GHz Radiometer at 40 km (-3 dB)
H, V, 3rd and 4th Stokes
Conical scan, fixed incidence angle at 40°
Contiguous 1000 km swath, 2-3 days revisit
Sun-synchronous 6am/6pm orbit (680 km)
Electronic Version at http://smap.jpl.nasa.gov/Imperative/
Print Version Available (182 Pages): smap_science@jpl.nasa.gov

## Slide 5
Soil Moisture Active/Passive (SMAP) Mission Concept
L-band unfocused SAR and radiometer system, offset-fed 6 m light-weight deployable mesh reflector. Shared feed for:
1.2 GHz Radar 1-3 km (30% nadir gap)
HH, VV and HV
1.4 GHz Radiometer at 40 km (-3 dB)
H, V, 3rd and 4th Stokes
Conical scan, fixed incidence angle at 40°
Contiguous 1000 km swath, 2-3 days revisit
Sun-synchronous 6am/6pm orbit (680 km)
Electronic Version at http://smap.jpl.nasa.gov/Imperative/
Print Version Available (182 Pages): smap_science@jpl.nasa.gov

## Slide 6
SMAP Launch: January 31, 2015

## Slide 7
First SMAP Measurements
http://smap.jpl.nasa.gov/news/1246/

## Slide 8
Current SMAP Data Product Summary |  | 
Data Product | Data Product Description | Gridding/ Resolution
L1A_Radiometer | Radiometer Data in Time-Order | -
L1B_TB | Radiometer TB in Time-Order | (36×47 km)
L1C_TB | Radiometer TB in Half-Orbits | 36 km
L1C_TB_E | Radiometer TB in Half-Orbits, Enhanced | 9 km
L2_SM_P | Soil Moisture (Radiometer) | 36 km
L2_SM_P_E | Soil Moisture (Radiometer, Enhanced) | 9 km
L2_SM_SP | Soil Moisture (Sentinel Radar + Radiometer) | 3 km
L3_FT_P | Freeze/Thaw State (Radiometer) | 36 km
L3_FT_P_E | Freeze/Thaw State (Radiometer, Enhanced) | 9 km
L3_SM_P | Soil Moisture (Radiometer) | 36 km
L3_SM_P_E | Soil Moisture (Radiometer, Enhanced) | 9 km
L4_SM | Soil Moisture (Surface and Root Zone) | 9 km
L4_C | Carbon Net Ecosystem Exchange (NEE) | 9 km
SMAP Data Product Table

## Slide 9
Soil moisture data assimilation: Updating dynamic and continuous model state predictions (dS/dt) using sporadic soil moisture observations (θ).
In its most common form:
S = Profile soil moisture and temperature states within a land surface model.
θ = Surface soil moisture retrievals from a satellite-based radar or radiometer.
Motivation:
Provides a spatially and temporally continuous soil moisture analysis.
Random errors in analysis ≤ those found in underlying model/observations.
Provides a mathematical basis for updating unobserved states.
Background/Motivation
Example system: The NASA Soil Moisture Active/Passive (SMAP) Level 4 (L4) Surface and Root-zone Soil Moisture Product.

## Slide 10
Soil moisture data assimilation: Updating dynamic and continuous model state predictions (dS/dt) using sporadic soil moisture observations (θ).
In its most common form:
S = Profile soil moisture and temperature states within a land surface model.
θ = Surface soil moisture retrievals from a satellite-based radar or radiometer.
Motivation:
Provides a spatially and temporally continuous soil moisture analysis.
Random errors in analysis ≤ those found in underlying model/observations.
Provides a mathematical basis for updating unobserved states.
Background/Motivation
Example system: The NASA Soil Moisture Active/Passive (SMAP) Level 4 (L4) Surface and Root-zone Soil Moisture Product

## Slide 11
Land Surface Model
SMAP L4 Surface and Root-Zone Soil Moisture Example

## Slide 12
Compare
Land Surface Model
SMAP L4 Surface and Root-Zone Soil Moisture Example
SMAP Satellite

## Slide 13
Compare
Update
Update all moisture and temperate states in model, not just those directly impacting SMAP measurements
Land Surface Model
SMAP L4 Surface and Root-Zone Soil Moisture Example
SMAP Satellite

## Slide 14
Benchmark rainfall (available > 1 week later)
Near real-time rainfall
SMAP L4 Surface and Root-Zone Soil Moisture Example

## Slide 15
Brightness temperature differences (SMAP minus model)
SMAP L4 Surface and Root-Zone Soil Moisture Example
Near real-time rainfall
Benchmark rainfall (available > 1 week later)

## Slide 16
Dynamic corrections to model states in response to observations
SMAP L4 Surface and Root-Zone Soil Moisture Example

## Slide 17
  Average:
  104,000 / day
  # assimilated obs. (4/2015 – 3/2017)
SMAP L4 Surface and Root-Zone Soil Moisture Example
9-km, hourly product, available since March 31, 2015 at ~2 to 3 day latency, output includes a wide range of land surface fluxes and states (ET, soil temperature, runoff, etc.)

## Slide 18
SMAP L4 Surface and Root-Zone Soil Moisture Example
Blue = Model, Red = Ground Obs., Black = SMAP L4

## Slide 19
SMAP L4 Validation at SMAP Ground Core Sites
SMAP core validation sites
Blue = Model, Black = SMAP L4

## Slide 20
http://nsidc.org/data/smap
Data Archive & HTML Doc
Product Specification Document
Algorithm Document
Data Assessment Reports
10.1175/JHM-D-17-0130.1
10.1175/JHM-D-17-0063.1
Peer-Reviewed Papers
(J. Hydromet.)
SMAP L4 Documentation
9-km, global land hourly product available since March 31, 2015 at ~2 to 3 day latency

## Slide 21
Sequential data assimilation (SMAP_L4) versus post-processing merging (SMERGE)
Sequential data assimilation:
1) Captures hourly/daily dynamics better.
2) Can estimate fluxes and states which are indirectly related to the observations.
Can horizontally-extrapolating spatially-discontinuous observations.
Computationally expensive for long-term products (1979-2015 SMERGE reprocessing would take on the order of ~1 year if run on single processor).
Labor consuming to develop and test systems (SMAP_L4 system took > 5 FTE’s to develop).
Han et al., HESS (2014) and Gruber et al., RSE (2017) argue that advantages #1 to #3 above do measurably add to the value of a root-zone soil moisture analysis for monthly agricultural drought monitoring
Therefore, SMERGE post-processing is: i) 100x faster to run, ii) 5x faster to develop and iii) likely as useful for agricultural drought applications.
SMERGE and NASA SMAP_L4 integration will be explored (once we have sufficient overlap)…

## Slide 22
Thank you…
Han, E., Crow, W.T., Holmes, T. and Bolten, J.D. Benchmarking a soil moisture data assimilation system for agricultural drought monitoring. Journal of Hydrometeorology. 15:1117-1134. 10.1175/JHM-D-13-0125.1. 2014.
Gruber, A. and Crow, W.T. The potential of 2D Kalman filtering for soil moisture data assimilation, Remote Sensing of Environment. 171:137-148. 10.1016/j.rse.2015.10.019. 2015.
Reichle, R. et al. Assessment of the SMAP Level-4 Surface and Root-Zone Soil Moisture Product using in situ measurements. Journal of Hydrometeorology. 18(10):2621-2645. 10.1175/JHM-D-17-0063.1. 2017.
Reichle, R. et al. Global assessment of the SMAP Level-4 surface and root-zone soil moisture product using assimilation diagnostics. Journal of Hydrometeorology. 18(12):3217-3237. 10.1175/JHM-D-17-0130.1. 2017.

## Slide 23
Compare
Update
Update all moisture and temperate states in model, not just those directly impacting SMAP measurements
Land Surface Model
SMAP L4 Surface and Root-Zone Soil Moisture Example
SMAP Satellite

## Slide 24
Compare
Update
Update all moisture and temperate states in model, not just those directly impacting SMAP measurements
Land Surface Model
SMAP L4 Surface and Root-Zone Soil Moisture Example
SMAP Satellite
GOOD
BAD

## Slide 25
Compare
Update
Update all moisture and temperate states in model, not just those directly impacting SMAP measurements
Land Surface Model
SMAP L4 Surface and Root-Zone Soil Moisture Example
SMAP Satellite
GOOD
BAD